Introduction to VHDL

---
VHDL
- DARPA, VHSIC (Very High Speed Integrated Circuits) program
- Different manufacturers
- Standard language to describe
  - Structure
  - Function
- VHDL (VHSIC Hardware Description Language)
- Based on ADA

---
VHDL
- Requirements
  - Describe structure
  - Specification
  - Simulation
  - Synthesis
- 1987, IEEE Standard 1076, VHDL-87
- Revisions:
  - 1992-1993, VHDL-93
  - 1998-2001, VHDL-2001
  - 2001-2008, VHDL-2008

---
Domains and Levels of Modeling

---
VHDL Modeling Concepts
- Entity
  - Black box
  - Describe connections of the module
  - Port types: in, out, inout
- Architecture
  - Define operation details
  - More than one architecture for each entity
entity reg4 is
port ( d0, d1, d2, d3, en, clk : in bit;
q0, q1, q2, q3 : out bit );
end reg4;

---
Behavioral Model
architecture behav of reg4 is
begin
storage : process is
variable stored_d0, stored_d1, stored_d2, stored_d3 : bit;
begin
if en = '1' and clk = '1' then
stored_d0 := d0;
stored_d1 := d1;
stored_d2 := d2;
stored_d3 := d3;
end if;
q0 <= stored_d0 after 5 ns;
q1 <= stored_d1 after 5 ns;
q2 <= stored_d2 after 5 ns;
q3 <= stored_d3 after 5 ns;
wait on d0, d1, d2, d3, en, clk;
end process storage;
end architecture behav;

---
Structural Model

---
Structural Model
entity d_latch is
port ( d, clk : in bit;
q : out bit );
end d_latch;
architecture basic of d_latch is
begin
latch_behavior : process is
begin
if clk = '1' then
q <= d after 2 ns;
end if;
wait on clk, d;
end process latch_behavior;
end architecture basic;
entity and2 is
port ( a, b : in bit;
y : out bit );
end and2;
architecture basic of and2 is
begin
and2_behavior : process is
begin
y <= a and b after 2 ns;
wait on a, b;
end process and2_behavior;
end architecture basic;

---
Structural Model
architecture struct of reg4 is
component d_latch is
port ( d, clk : in bit;
q : out bit );
end component;
component and2 is
port ( a, b : in bit;
y : out bit );
end component;
signal int_clk : bit;
begin
bit0 : d_latch port map(d => d0, clk => int_clk, q => q0);
bit1 : d_latch port map(d => d1, clk => int_clk, q => q1);
bit2 : d_latch port map(d => d2, clk => int_clk, q => q2);
bit3 : d_latch port map(d => d3, clk => int_clk, q => q3);
gate : and2 port map(a => en, b => clk, y => int_clk);
end architecture struct;

---
Lexical elements
- Comment
  variable data : bit; --description of variable data
  --this is a long ...
  --... long comment
- Identifiers
  - 'A' to 'Z', 'a' to 'z', '0' to '9' and '_'
  - Must start with an alphabetic letter
  - No successive underlines, not end with underline
  - Case insensitive: Cat, CAT, cat, CaT are the same

---
Numbers
- Decimal literals
  - 23, 0, 146
- Real literals
  - 23.1, 0.0, 3.14159
  - 46E5, 1E+12, 34.0e-08
- Number base
  - 2#111111011#, 16#FD#, 16#0fd#, 8#0375#
  - 2#0.1000#, 8#0.4#, 12#0.6#
- 123_456, 3.141_592_6, 2#1111_1100#

---
Characters, strings, bit strings
- Characters
  - 'A', 'z', ',', ''', ' '
- Strings
  - "A string", "" --empty string
- Bit strings
  - Binary, B"0110001", b"0110_0111"
  - Octal, O"372", o"00"
  - Hex, X"FA", x"0d"

---
Predefined types
- Enumeration type
  - Bits: type bit is ('0', '1');
- Integer
  - 32bit singed integer
- Real
  - 32bit single precision floating point number
- Physical type
  - Time: 1fs
- Type conversion
  real(123)
  integer(1.23)

---
Signal, Constant and Variable declaration
signal identifier {, ...}: subtype_indication [:= expression];
constant identifier {, ...}: subtype_indication [:= expression];
variable identifier {, ...}: subtype_indication [:= expression];
signal d_reg : bit := ’1’;
signal accumulator : integer := 0;
constant number_of_bytes : integer := 4;
constant number_of_bits : integer := 8* number_of_bytes;
constant e : real := 2.718281828;
constant prop_delay : time := 3 ns;
constant size_limit, count_limit : integer := 255;
variable index : integer := 0;
variable sum, average, largest : real;
variable start, finish : time := 0 ns;

---
Expressions and operators
** exponentiation
abs absolute value
not negation
* multiplication
/ division
mod modulo
rem remainder
+ identity
- negation
+ addition
- subtraction
& concatenation
sll shift-left logical
srl shift-right logical
sla shift-left arithmetic
sra shift-right arithmetic
rol rotate left
ror rotate right
= equality
/= inequality
< less than
<= less than or equal
> greater than
>= greater than or equal
and logical and
or logical or
nand negated logical and
nor negated logical or
xor exclusive or
xnor negated exclusive or

---
Type declarations
- type identifier is type_definition
- Integer types
  type_definition <= range expr. (to | downto) expr.
  type apples is range 0 to 100;
  type oranges is range 0 to 100;
  oranges:=apples; --illegal!!!
  constant number_of_bits : integer :=32;
  type bit_index is range 0 to number_of_bits-1;

---
Subtypes
- subtype identifier is type_mark [ range expr. (to | downto) expr.]
- Predefinied subtypes
  - subtype natural is integer range 0 to highest_integer;
  - subtype positive is integer range 1 to highest_integer;

---
Floating-point types
type_definition <= range expr. (to | downto) expr.
type input_level is range -10.0 to +10.0;
type probability is range 0.0 to 1.0;

---
Physical types
range expr. (to | downto) expr.
units
identifier;
{identifier = physical_literal;}
end units [identifier];
physical_literal <= [decimal_literal | based_literal] unit_name

---
Physical types
type resistance is range 0 to 1E9
units
ohm;
end units resistance;
type length is range 0 to 1E9
units
um;	--primary unit micron
mm=1000 um;	--metric units
m=1000 mm;
inch=25400 um;	--English units
foot=12 inch;
end units length;

---
Physical types
type time is range impl. def.
units
fs;
ps=1000 fs;
ns=1000 ps;
us=1000 ns;
ms=1000 us;
sec=1000 ms;
min=60 sec;
hr=60 min;
end units;

---
Arrays
- type type_name is array (expr ( to | downto) expr) of subtype;
  - type word is array (0 to 31) of bit
  - type word is array (31 downto 0) of bit;
- type type_name is array (natural range <>) of subtype;
  - type bit_vector is array (natural range <> ) of bit;
  - signal csr_offset : bit_vector(2 downto 1);

---
Library and package
library ieee;
use ieee.std_logic_1164.all;
- Standard types, operators, functions
  - std_logic, std_logic_vector
  use ieee.numeric_std.all;
- Signed and unsigned types, operators, functions

---
Standard logic
- Standard logic
  type std_ulogic is (
  ’U’, --Uninitialized
  ’X’, --Forcing unknown
  ’0’, --Forcing 0
  ’1’, --Forcing 1
  ’Z’, --High impedance
  ’W’, --Weak unknown
  ’L’, --Weak 0
  ’H’, --Weak 1
  ’-’, --Don’t care
  );

---
Architecture Body
architecture identifier of entity_name is
{block_declarative_item}
begin
{concurrent_statement}
end [architecture][identifier];

---
Process statement
[process_label:]
process [(signal_name{,…}|all)] [is]
{process_declarative_item}
begin
{sequential_statement}
end process [process_label];

---
Variable and signal assignment
signal s_y : std_logic;
variable v_y : std_logic;
s_y <= not (a or b) after 5 ns;
v_y := not (a or b);

---
If statement
[if_label:] if boolean_expression then
{sequential_statement}
{elsif boolean_expression then
{sequential_statement}}
{else boolean_expression
{sequential_statement}}
end if; [if_label];

---
If statement
if en = '1' then
stored_value := data_in;
end if;
if sel = 0 then
result <= input_0; -- executed if sel = 0
else
result <= input_1; -- executed if sel /= 0
end if;

---
If statement
type mode_type is (immediate, other_mode);
type opcode_type is (load, add, subtract, other_opcode);
if mode = immediate then
operand := immed_operand;
elsif opcode = load or opcode = add or opcode = subtract then
operand := memory_operand;
else
operand := address_operand;
end if;

---
Case statement
[case_label:] case expression is
(when choices => {sequential_statement})
{...}
end case [case_label];
choices <= (simple_expression | discrete_range | others){ | ...}

---
Case statement
type alu_func is (pass1, pass2, add, subtract);
case func is
when pass1 =>
result := operand1;
when pass2 =>
result := operand2;
when add =>
result := operand1 + operand2;
when subtract =>
result := operand1 - operand2;
end case;

---
Case statement
type opcodes is (nop, add, subtract, load, store, jump, jumpsub, branch, halt);
subtype control_transfer_opcodes is opcodes range jump to branch;
case opcode is
when load | add | subtract =>
operand := memory_operand;
when store | jump | jumpsub | branch =>
operand := address_operand;
when others =>
operand := 0;
end case;

---
Null statement
type opcode_type is (nop, add, subtract);
case opcode is
when add =>
Acc := Acc + operand;
when subtract =>
Acc := Acc - operand;
when nop =>
null;
end case;

---
Loop, For loop and While loop
[loop_label:]
loop
{sequential_statement}
end loop [loop_label];
[loop_label:]
while boolean_expression loop
{sequential_statement}
end loop [loop_label:];
[loop_label:]
for identifier in discrete_range loop
{sequential_statement}
end loop [loop_label];

---
Exit and next statement
loop
if condition then
exit;
end if;
end loop;
loop
exit when condition;
end loop;
next;
next when condition;
next loop_label;
next loop_label when condition;

---
Discrete event simulation
- Transaction
  - After signal assignment, new value at simulation time T
- Active signal
  - Signal is updated at time T
- Event
  - New value /= old value

---
Discrete event simulation
- Initialization phase
  - Each signal is given an initial value
  - Simulation time is set to 0
  - Each process is activated
  - Signals assigned, transactions scheduled
- Simulation cycle
  - Signal update
    - Advance time to the next transaction
    - Perform all scheduled transactions for this time
  - Process execution
    - Wake processes which is sensitive to the previous events
    - New events may occur

---
Delta delay
- Signal assignment without after equivalent to a delay of 0 fs
- BUT the signal value does not change as soon as the signal assignment statement is executed
- Assignment schedules a transaction for the signal
- The process does NOT see the effect of the assignment until it next time resumes

---
Signal attributes
S'event
  - True if there is an event on S in the current simulation cycle, false otherwise
S'active
  - True if there is a transaction on S in the current simulation cycle, false otherwise
S'last_event
  - The time interval since the last event on S
S'last_active
  - The time interval since the last transaction on S
S'last_value
  - The value of S just before the last event on S

---
Test Benches

---
Test Benches
entity test_bench is
end entity test_bench;
architecture test_reg4 of test_bench is
signal d0, d1, d2, d3, en, clk, q0, q1, q2, q3 : bit;
begin
dut : entity work.reg4(behav)
port map ( d0, d1, d2, d3, en, clk, q0, q1, q2, q3 );
stimulus : process is
begin
d0 <= '1'; d1 <= '1'; d2 <= '1'; d3 <= '1';
en <= '0'; clk <= '0';
wait for 20 ns;
en <= '1'; wait for 20 ns;
clk <= '1'; wait for 20 ns;
d0 <= '0'; d1 <= '0'; d2 <= '0'; d3 <= '0'; wait for 20 ns;
en <= '0'; wait for 20 ns;
-- . . .
wait;
end process stimulus;
end architecture test_reg4;

---
Latch With Positive Gate
process(G,D)
begin
if G=’1’ then
Q <= D;
end if;
end process;

---
D Flip-Flop
process(c)
begin
if c’event and c=’1’ then
q <= d;
end if;
end process;

---
D Flip-Flop and asynchronous reset
process(c,clr)
begin
if clr=‘1’ then
q <= ‘0’;
elsif c’event and c=‘0’ then
q <= d;
end if;
end process;

---
D Flip-Flop and Synchronous Set
process(c)
begin
if c’event and c=‘1’ then
if s=‘1’ then
q <= ‘1’;
else
q <= d;
end if;
end if;
end process;

---
D Flip-Flop and Clock Enable
process(c)
begin
if c’event and c=‘1’ then
if ce=‘1’ then
q <= d;
end if;
end if;
end process;

---
D Flip-Flop, Asynchronous Set, and Clock Enable
process(c,pre)
begin
if pre=‘1’ then
q <= ‘1’;
elsif c’event and c=‘1’ then
if ce=’1’ then
q <= d;
end if;
end if;
end process;

---
Tristate buffer
process(I,T)
begin
if T=’0’ then
O <= I;
else
O <= ’Z’;
end if;
end process;

---
4-to-1 1-Bit MUX Using IF Statement
process(a,b,c,d,s)
begin
if s="00" then o<=a;
elsif s="01" then o<=b;
elsif s="10" then o<=c;
else o<=d;
end if;
end process;

---
4-to-1 1-Bit MUX Using Case Statement
process(a,b,c,d,s)
begin
case s is
when "00" => o<=a;
when "01" => o<=b;
when "10" => o<=c;
when others => o<= d;
end case;
end process;

---
The Xilinx Spartan-3E FPGA family

---
Field Programmable Gate Array (FPGA)
- Configurable Logic Block (CLB)
  - Look-up table (LUT)
  - Register
  - Logic circuit
    - Adder
    - Multiplier
    - Memory
    - Microprocessor
- Input/Output Block (IOB)
- Programmable interconnect

---
Xilinx FPGA families
- High performance
  - Virtex (1998)
    - 768-12.2K LC, 0.22µm
  - Virtex-E/EM (1999)
    - 768-32.4K LC, 0.18µm
  - Virtex-II (2000)
    - 512-93.1K LC, 0.15µm
  - Virtex-II Pro/X (2002)
    - 2.8K-111.2K LC, 0.13µm
  - Virtex-4 (2004) [LX, FX, SX]
    - 12.2K-178.1K LC, 90nm
  - Virtex-5 (2006) [LX, LXT, SXT]
    - 19.2-207.3K LC, 65nm
  - Virtex-6 (2009) [LXT, SXT, HXT]
    - 46.5K-474.2K LC, 40nm
  - Virtex-7 (2010)
    - 178.8K-1.22M LC, 28nm
  - Virtex UltraScale (2013)
    - 783K-5.541M LC, 20nm
  - Virtex UltraScale+ (2015)
    - 862K-3.780M LC, 16nm
- Low cost
  - Spartan-II (2000)
    - 0.22µm
  - Spartan-IIE (2001)
    - 0.18µm
  - Spartan-3 (2003)
    - 1.5K-66.5K LC, 90nm
  - Spartan-3E (2005)
    - 1.9K-29.5K LC, 90nm
  - Spartan-6 (2009)
    - 1.5K-92.1K LC, 45nm
  - Artix-7 (2010)
    - 11.2K-220K LC, 28nm
- Mid-range
  - Kintex-7 (2010)
    - 19K-254K LC, 28nm
  - Kintex UltraScale (2013)
    - 318K-1.451M LC, 20nm
  - Kintex UltraScale+ (2015)
    - 356K-1.143M LC, 16nm

---
Programmable Logic (PL) Description
- CLB
  - Eight LUTs per CLB for random logic implementation or distributed memory
  - Memory LUTs are configurable as 64x1 or 32x2 bit RAM or shift register (SRL)
  - 16 flip-flops per CLB
  - 2 x 4-bit cascadeable adders for arithmetic functions
- 36 Kb block RAM
  - True dual-port
  - Up to 36 bits wide
  - Configurable as dual 18 Kb block RAMs
- DSP slices
  - 18 x 25 signed multiply
  - 48-bit adder/accumulator
- Programmable I/O Blocks
  - Support for common I/O standards including LVCMOS, LVDS, and SSTL
  - 1.2V to 3.3V I/O
  - Built-in programmable I/O delay
- Low-power serial transceivers in selected Zynq-7000 All Programmable SoCs
- An integrated Endpoint/Root port (can be Root Complex when connected to the PS) block for PCI Express in selected Zynq-7000 All Programmable SoCs
- Two 12-bit analog to digital converters (XADC)
  - On-chip voltage and temperature
  - Up to 17 external differential input channels
- PL configuration module

---
Spartan-3E architecture

---
Interconnect Types

---
Resources in a Slice

---
Carry Logic

---
Xilinx 7 Series FPGA Logic resources
- 6 input LUT
  - 5 input 2 output LUT
  - 32bit shift register
  - 64bit RAM
- 8 register
- 4 carry logic
- 2:1 multiplexers
  - 7, 8 input LUT
  - 128, 256 bit RAM
  - 8:1, 16:1 multiplexer

---
Block RAM

---
Xilinx 7 Series FPGA Dedicated resources, Block RAM
- 36kbit dual ported SRAM (32k x 1 - 512 x 72)
- Can be configured as two 18kbit independent SRAM
- Dedicated FIFO logic

---
Dedicated 18x18bit Multiplier

---
Xilinx 7 Series FPGA Dedicated resources
- DSP48E1 block
  - 25x18bit signed multiplier
  - 48bit adder/accumulator, ALU

---
Resource comparison
	Virtex-7	Artix-7	Kintex-7	Zynq-7000	Kintex UltraScale+	Virtex UltraScale+	Zynq UltraScale+ MPSoC EG
Slice	305,400	55,050	74,650	69,350	130,680	432,000	130,680
BRAM 36Kbit URAM 288Kbit	1,800	335	955	755	984 + 128	2,688 + 1,280	984 + 128
Mult / 18x25bit	3,960	700	1,920	2,020	3,528	12,288	3,528
I/O / Max. / 2400MHz	1,200	450	500	350	572 + 96	832	572 + 120
Serial I/O / Max. / 28Gb/s	72 + 16	4	32	12	44 + 32	128	44 + 28