Introductory project

---
Design Flow
- Design Entry
  - Vivado
  - Vivado HLS
  - Third party tools
    - Mentor Graphics: FPGA Advantage
- Design Synthesis
  - XST: Xilinx Synthesis Technology
  - Vivado HLS
  - Mentor: Leonardo Spectrum
  - Synplicity: Synplify Pro
- Simulation
  - Xilinx: ISIM
  - Mentor: Modelsim

---
Design Verification
- Behavioral Simulation
  - Checking high level description of the circuit
- Functional Simulation
  - Checking synthesized circuit
- Timing Simulation
- Static Timing Analysis
  - Searching critical paths
- In-Circuit Verification

---
Design Flow
- Optimization
  - Merge multiple design files into a single netlist
- Mapping
  - Group logical symbols from the netlist (gates) into physical components (slices and IOBs)

---
Design Flow
- Place & Route:
  - Place components onto the chip, connect the components, and extract timing data into reports
- Bitstream Generation
  - Create configuration file

---
Start Vivado HLS
- Use command line
  - Open terminal (CTRL-ALT-T)
  - Run /home/shared/vivado_2018.3.sh
- Use dash
  - Click on first icon in the toolbar or press Windows button
  - Start typing: vivado
  - Click on Vivado icon

---
Create new project

---
Click Next

---
Choose project directory and name (myand2)

---
Click Next

---
Select target language: VHDL
Click on Next

---
Click Next

---
Click on Boards

---
Select: ZedBoard Zynq Evaluation and Development Kit

---
Click on Finish

---
Vivado main window

---
Select Add or create design sources

---
Click on Create File

---
Set File type: VHDL
- Set File name: myand2
- Click Finish

---
Click Finish

---
Define Module Ports
- Add two input ports: a, b
- Add output port: c

---
New source is added
Add another source

---
Select Add or create constraints

---
Click on Create File

---
Set File type: XDC
Set File name: myand2

---
Click Finish

---
Open VHDL source and edit

---
Language Templates

---
Create yet another new source
Select Add or create simulation sources

---
Click on Create File

---
Set File type: VHDL
Set File name: myand2_tb

---
Click Finish

---
No ports required for testbench

---
Write Testbench

---
Write Testbench
architecture Behavioral of myand2_tb is
component myand2 is
  Port ( a : in STD_LOGIC;
        b : in STD_LOGIC;
        c : out STD_LOGIC);
end component;
signal a_sig : STD_LOGIC := '0';
signal b_sig : STD_LOGIC := '0';
signal c_sig : STD_LOGIC;
begin
uut: myand2 PORT MAP (
a => a_sig,
b => b_sig,
c => c_sig
);
stim_proc: process
begin
wait for 100ns;
a_sig <= '1';
b_sig <= '0';
wait for 10ns;
a_sig <= '1';
b_sig <= '1';
wait for 10ns;
a_sig <= '0';
b_sig <= '1';
wait for 10ns;
a_sig <= '0';
b_sig <= '0';
wait;
end process;
end Behavioral;

---
Run Behavioral Simulation

---
Check simulation results

---
Before implementation
- Set pin constraints!
- Master XDC file for ZedBoard
- https://wiki.itk.ppke.hu/twiki/pub/PPKE/DigitalisAramkörökTerv/zedboard_master_XDC_RevC_D_v3.xdc
- http://zedboard.org/support/documentation/1521

---
Set constraints in XDC
- Search LEDs, DIP Switches and IOSTANDARD constraints in master XDC
- Port names must be updated! (LD0 → c)

---
Run Synthesis

---
Select Open Synthesized Design

---
Synthesized Design

---
Run Implementation
Select Open Implemented Design

---
Implemented Design

---
Design layout

---
Routing resources

---
Generate Bitstream
- When Bitstream Generated select Open Hardware Manager and turn on ZedBoard
- Click on Open target and select Auto connect
- Click on Program Device and select the FPGA (xc7z020_1)
- Push Program
- The blue led on the board shows that the FPGA is configured
- Test your first FPGA design using the switches

---
Full Adder

---
4-bit Ripple Carry Adder