## Slide 1: Infokommunikációs rendszerek Infocom Systems 5. Nyilvános távbeszélő (PSTN) hálózatok, gerinchálózatok Telephone networks(PSTN), backbone networks
Takács György

## Slide 2: The 3 lessons in network studies
Public Switched Telephone Networks (PSTN), Integrated Service Digital Networks (ISDN), backbone networks
Mobile Networks -- Public Land Mobile Networks (PLMN) GSM, UMTS, DECT, TETRA, Bluetooth, Globalstar, Iridium
Private networks, Broadcasting networks, Cable TV networks (CaTV)

## Slide 4: Flash report on landline services for August 2017

## Slide 5: Flash report on landline services for August 2017

## Slide 8: Number of mobile Internet subscriptions (pc)

## Slide 11: Special features of networks
Only services can be sold on the real market!
There are not infocommunication services without networks.
You could not buy networks. You have to plan, to construct, to operate, to develope according to the actual demands and to eliminate at the and of service provision.

## Slide 12
v
Service, application and content providers….
Like: Vodafone, CIB Bank, CNN
Servers
Network operators
Transmission lines,
Multiplexers,
Routers,
Switches
End users
Like: subscribers,
Companies
Mobile sets, TV sets,
computers

## Slide 13: Basics of network components
Backbone networks: long distances, high traffic, interconnection of nodes, transport bits of any services, high relability, high availability.
Access networks: local distances, interconnection of terminals and local nodes
Network planning: selecting topology, optimal selection of positions of nodes, dimensioning of node traffic handling capacities, dimensioning of link capacities, selecting technologies.

## Slide 17
The pan European KPNQwest network, when complete, will connect major cities together by six high-capacity backbone rings.

## Slide 19
AOL USA BACKBONE

## Slide 25: Public Switched Telephone Networks (PSTN)
Brief history
Basics
Network structures
Network implementation
Network development trends
Missing topics

## Slide 26: Brief history I.
1876 A. G. Bell Patent of telephone (50.000 phone within 3 years)
1877 T. A. Edison patent of carbon microphone (covering long distances)
1878 Puskás Tivadar the first telephone exchange in Connecticut
1881 Puskás Ferenc the first telephone exchange in Budapest
1890 The first Wien-Budapest international telephone connection
1892 The first automatic telephone exchange in Indiana
1928 The first automatic telephone exchange in Budapest
1997 The last manual exchange moved to museum in Hungary

## Slide 28: Brief history II.
The technical level of Hungarian PSTN networks are very high due to the fast development from 1992-2002
From 1 million subscriber to 10 million one
From 1000 manual exchange to almost fully digital network
COCOM list restriction not from our side!!!

## Slide 29: Basics of telephony
2/4 wire for voice
Feeding of circuit
Access solutions
Backbone
Signalling basics for a telephone call
Source of revenues
ADSL principles

## Slide 30: 2/4 wire for voice
2 wire simplex
2 wire duplex
4 wire simplex

## Slide 31: Electronic hybrid circuit
ZT
Zg
r
r
Twisted pair cable
Z0 characteristic impedance
ZT ~Z0

## Slide 32: Powering of telephone sets
Feeding bridge
Subscriber line
Local exchange
Traditional feeding bridge circuit
DC line current: 20….60 mA

## Slide 33: Access solutions

## Slide 34: Connections to the local exchange
Distribution cables
Drop cables,
Indoor cables
Main cables
Distribution cabinets
Distribution boxes

## Slide 35: Access network implementation

## Slide 36: Cable duct system implementation

## Slide 37: Cable distribution cabinet (street version) implementation

## Slide 38: Signalling basics for a telephone call

## Slide 39: Channel-associated signalling for a trunk call

## Slide 40: Common-channel signalling for a trunk call

## Slide 41: Backbone issues in a small country with dense population
Fully optical – only spare radio connections
Covered distance between nodes max 100 km
In Hungary the source of telecom traffic (including telephone, TV programs, Internet) concentrated in Budapest (like the road traffic)
Concentration of switching capacities in higher level nodes
Fault tolerant topology is required for reliable services

## Slide 42: Network structures
Basics
MATÁV structures
PANTEL structures
Interconnection issues
Structure and numbering
Intelligent Network Concept

## Slide 43: Basic structures in PSTN/ISDN networks
Star topology
Multipolar topology
Meshed topology
Ring topology
Bus topology

## Slide 44
STAR
BUS
RING
MESHED
MULTIPOLAR

## Slide 45: MATÁV NETWORK STRUCTURE

## Slide 46
Telephone network structure of MATAV
Secondary exchange
Primary exchange
Backbone
network
Local
exchange
Subscriber
Access
network
Inter
exchange
network

## Slide 50
Layer
Physical layer
Optical cable
2. Layer
Data link layer
IP link
3. Layer
Network layer

## Slide 51: PANTEL optical backbone structures

## Slide 52: PANTEL logical SDH rings

## Slide 53
Interconnection principles

## Slide 54
Interconnection principles

## Slide 55
Interconnection implementation

## Slide 56: Network structure and numbering

## Slide 57: Network implementation
Access issues: Rural, City, Down-town, areas, In-door cabling, Underground copper cables, Overhead cables, ADSL, Fibre To the Curb (FTC), distribution frames
Core issues: Underground fibres, overhead fibres,
Switching and multiplexing position of nodes
Traffic issues: dimensioning of switches and links

## Slide 58: Access network implementation

## Slide 59: Costs and revenues –> market failure The revenues are monthly fees and traffic based fees Networ costs are implementation and operation
Traffic density (Erlang/km2
Network costs
Wireline networks
Cellular networks

## Slide 60: Telephone bill balance
balance
time
Pre-paid
balance
time
balance
time
Post-paid

## Slide 62: Missing topics
Telephone sets, terminal equipment (Lecture in Nov )
Services (Lecture in Nov )
Regulation issues (Lecture in November )
Details of ADSL
NGN (Next Generation Networks in December)
Network planning (optional subject in semester 7.)

## Slide 63
Traditional Solutions in
Services
Access Transport & Switching Networks
CATV
PLMN
PSTN/ISDN
Data/IP Networks
PLMN
PSTN/ISDN
Data/IP
Networks
CATV
Services/Applications
Connectivity
Future Solutions
Network development trends